## Slide 1: MUTHAYAMMAL ENGINEERING COLLEGE DEPAERTMENT OF MEDICAL ELECTRONICS Electromyography 10/9/2019 A.SIVA SANKAR AP/MDE

## Slide 2: Outline
Muscle Moment – Moment Arm
Review of Muscle Contraction Physiology
Physiological Basis of EMG
Methods of EMG Collection
Limitations & Uses
(DHHS 91-100 chapter 2 and 5)
Journal of Electromyography and Kinesiology (full-text in ScienceDirect)

## Slide 3: What is EMG
Muscle contraction due to a change in the relative sliding of thread-like molecules or filaments
    Actin and Myosin
Filament sliding is triggered by electrical phenomenon (ACTION POTENTIAL, AP)
The recording of muscle APs is called electromyography (EMG)
    The record is known as an electromyogram

## Slide 4: Action Potential (AP)
Cell membrane separates intracellular from extracellular space, diffusion barrier which restricts ION flow. Concentration of ions different inside vs. outside of cell membrane, results in an electrical potential difference known as a MEMBRANE POTENTIAL. Typical magnitude of membrane potential is -60 and -90 mV (interior of cell is negatively charged compared to the outside) when the muscle cell is in resting state.
When sufficient neurotransmitters are deposited at the motor endplate, it opens up Na+ gates, causing an influx of Na+ ions, causing a rapid depolarization of the membrane near the motor end plate. The membrane potential can change to +20 to +50 mV at the motor endplate within a fractions of a second, which starts (all or none) a cascade of events.

## Slide 5: Action Potential (continued)
http://upload.wikimedia.org/wikipedia/en/thumb/7/78/Apshoot.jpg/300px-Apshoot.jpg

## Slide 6: AP Continued
This changed potential, sets up local currents in adjacent areas of membrane, which opens up more Na+ gates at the adjacent areas of the membrane, depolarizing those areas. The newly depolarized areas sets up electrical current with adjacent areas, and thus the depolarization wave propagates along the entire length of the muscle cell.
Shortly after depolarization, the membrane is again repolarized, by active transport (ATP expenditure) of ions across the membrane. As a result a repolarization wave follows the depolarization wave for the entire length of the muscle.

## Slide 7: Action Potential Summary
Active response of excitable membranes in nerve and muscle fibers produced by sodium and potassium channels opening in response to a stimulus
AP abide by the all-or-none principle
  If MP reaches threshold voltage then Na+ channels open at first (Which direction will Na+ flow?)
  Na+ channels only open for 1 ms, this causes repolarization (K+ channels also open during this time to speed up return of resting membrane potential)
  AP propagation along muscle fibers
AP propagation velocity dependent upon:
(1) diameter of fibers (faster for thick – fast twitch)
(2) [K+] in extracellular fluid, ie chemical environment.

## Slide 8: Motor Unit Action Potential
Typically, each motorneuron innervates several hundred muscle fibers (innervation ratio)
Motor Unit Action Potential (MUAP) = summed electrical activity of all muscle fibers activated within the motor unit
Muscle force increased through higher recruitment and increased rate coding

## Slide 9: Recording Methodology
Sweep of AP  similar to a wave
Height of wave and the density of the wave can be recorded
Represented graphically  electromyogram

## Slide 10: Recording Methodology (continued)
Electrical potential difference measured between two points  bipolar electrode configuration used
Bipolar Electrode Types
    Fine Wire
    Needle
    Surface
      Most common, less invasive
      Silver-silver chloride electrodes
Electrode Placement
    Overlying the muscle of interest in the direction of predominant fiber direction
    Subject is GROUNDED by placing an electrode in an inactive region of body
http://www.hhdev.psu.edu/atlab/EMG.jpg

## Slide 11: EMG Electrodes
Fine wire
Surface Electrodes
Needle electrode

## Slide 12: Physiological Basis
Hypothetical EMG from a single Muscle cell

## Slide 13: Physiological Basis
Hypothetical EMG from a Motor unit

## Slide 14: Typical EMG recording
Time axis (msec) 
Amplitude (mv)
Average amplitude over a time interval = 0

## Slide 15: Analyzing the EMG Signal
Amplitude & Frequency
More MU  more amplitude, more spikes and more turns in signal
Change in firing rate  change in frequency content of EMG
Change in muscle fiber type  change in AP velocity, change in EMG frequency.
EMG is spatial and temporal summation of APs

## Slide 16: Average Rectified Amplitude
Rectified = all negative values converted to positive values (absolute value)
Then the average rectified amplitude provides a measure of signal strength

## Slide 17: EMG Amplitude vs Muscle Contraction Intensity
Amplitude increases with increased contraction intensity, BUT it is not a linear relationship

## Slide 18: RMS Amplitude
RMS (Root Mean Square):
  Each data point is squared and thus the negative values becomes positive.
  Mean is determined from the squared values
  Square root of this mean is RMS

## Slide 19: Factors Influencing Signal Measured
Geometrical & Anatomical Factors
  Electrode size
  Electrode shape
  Electrode separation distance with respect to muscle tendon junctions
  Thickness of skin and subcutaneous fat
  Misalignment between electrodes and fiber alignment
Physiological Factors
  Blood flow and temperature
  Type and level of contraction
  Muscle fiber conduction velocity
  Number of motor units (MU)
  Degree of MU synchronization

## Slide 20: Effect of electrode position on EMG

## Slide 21: Normalization
Def: calibration against a known reference
This allows researchers ability to compare different activities for the same muscle, different muscles, activities on different days, different subjects for same or different tasks, etc.
Choices of normalization
      Maximum voluntary contraction (MVC)
        Functional activty
        Isometric activty
      Unresisted normal activity
      Submaximum contraction
Limitations
      Variability of force generation due to motivation/physiological reasons

## Slide 22: What can be learned from an EMG?
Time course of muscle contraction
Contraction force
Coordination of several muscles in a movement sequence
    These parameters are DERIVED from the amplitude, frequency, and change of these over time of the EMG signal
Field of Ergonomics: from the EMG conclusions about muscle strain and the occurrence of muscular fatigue can be derived as well